## Slide 1
  Haptic Implementation on Deformable Objects based on Oriented Particles
Presenter：Haiyang Ding
E-Mail: teikaiyo@haselab.net
Tokyo Institute of Technology
Precision & Intelligence Laboratory
Multi-soft-body objects
interaction (only use CPU)
Algorithm:
Simulation Step:
-Prediction Step:
--Particle’s position and orientation
are predicted as , , using velocity and angular velocity of the last step.
-Solve collision constraint;
-Constraints iteration:
--Solve shape-matching[2005 Müller]
constraint (deformation);
--Solve other constraints
--Solve proxy for haptic
(therefore, predicted position and orientation are been corrected into and respectively by constraints)
-Haptic force calculation
-Integration
--Velocity and angular velocity
are updated by corrected ones
--Particle‘s position and
orientation are updated by
the corrected ones ,
respectively.
Detailed haptic interaction:
By binding meshes to particle, we propose a two-layer collision detection for haptic proxy;
Particle collision
Local meshes collision
Oriented Particles(OP) [2011 Müller] is a fast and robust geometric deformation method which is suitable for multi-soft object and robust simulation. Particles are grouped as a particle net for a model. One particle controls a certain numbers of model vertices.
Future Application:
Soft-body Surgery Simulation. 1*
Multi-soft-object Haptic Game.
(UFO catcher) 1*
Device end-effector
Proxy
Particle
1
2
Simulation Screenshot
Untouched
touched
1
2
Large deformation is
correctly performed
compare to linear-FEM
1*. Pictures are from Internet
Bunny model is
assigned with
particles
1
2
3
4
layer
layer
Haiyang Ding, Hinorori Mitake, Shoichi Hasegawa.
Future Work: 6-DOF rendering
Original
Deformed
Match rotation
Shape matched
Shape-matching algorithm
F
Shape-matching with multi- clusters
F
Notes: Background : importance of this two

## Slide 2
  Haptic Implementation on Deformable Objects based on Oriented Particle
Presenter：Ding Haiyang
E-Mail: teikaiyo@haselab.net
Tokyo Institute of Technology
Department of Computational Intelligence and Systems Science
Soft-body Surgery Simulation
Oriented Particle :
Robust deformation
Fast
Rough collision
Multi-soft-body objects interaction (only use CPU)
inside
outside
1
2
Notes: Background : importance of this two

## Slide 3
研究タイトル：方向つき粒子による柔軟物の力覚レンダリング
  Research Title:
  Haptic Rendering for Deformable Objects based on Oriented Particle
長谷川晶一研究室
発表者：Ding Haiyang
E-Mail: teikaiyo@haselab.net
東京工業大学
総合理工研究科
知能システム専攻
従来と提案の安定性評価
変形物との頑丈、安定なインタラクション
柔軟体との力覚インタラクションシステム
例：手術訓練システム
計算量を減らすため、
高速な変形手法の
力覚レンダリング手法
を提案する
リアルライム
計算が大変
Position based dynamicsベースの
安定な力覚レンダリング
発振が収まった
大変形に対応
Notes: Background : importance of this two

## Slide 4
Proxy particle
particles
Particle collision
Local Mesh
collision
1
2
Haptic pointer
Surface mesh

## Slide 5
inside
outside

## Slide 6
私は以下の時間帯には
必ずこのボードの前におります．
不在の場合は改めて来て頂ければ，
ポスター発表を行わせて頂きます．
I will be here during
１３：００ ～ １４：００ まで

## Slide 7
私は以下の時間帯には
必ずこのボードの前におります．
不在の場合は改めて来て頂ければ，
ポスター発表を行わせて頂きます．
I will be here during
１４：００ ～ １５：００ まで

## Slide 8
私は以下の時間帯には
必ずこのボードの前におります．
不在の場合は改めて来て頂ければ，
ポスター発表を行わせて頂きます．
I will be here during
１５：００ ～ １６：００ まで